AndrOBD V1.2.x
faster, more colorful, customizable

# New Features of V1.2.0:
- CSV based control data for
  - Data items / PIDs
  - Data conversions
  - code lists
- new Conversion types
  - Bitmap conversions for bit mapped states
  - Hash conversion for numeric states
- bar gauge display in data screen
- consistent coloring of data items in
  - data display
  - data charts
  - gauge / hud display
- Data Customization
  - Following OBD data can be customized via user defined csv files
    - data conversions
    - data items/PIDs
    - fault code lists
- Configuration
  - Display off in data display configurable
  - Debug / Customization configuration
    - Logging level
    - Selection of extension/customization files
      - data conversions
      - data items/PIDs
      - fault code lists

# Configuration data:
The data model is split into 3 different files, which are all in tab-delimited csv format:
- code lists
- Data conversions
- Data items / PIDs

## Code lists:
Code list definitions contain all data to convert a reported DFC (Diagnostic Fault Code) into it's meaningful text description. It is basically just a mapping list of P/I-Code numbers to their descriptions.
### Code list data fields:
Since it is just a 2-field list, the columns do not have a header.
Column	Description
1	DFC number
2	DFC description

## Conversions:
The conversion data contains all information which is required to convert a incoming data value into a physical, or textual representation value. Since there are multiple methods to convert binary data to meaningful information, several conversion types are supported. Also there are different measurement systems used around the world, so following, most common measurement systems are supported: metric and imperial.

### Conversion types:
In order to convert protocol data into numerical, or textual values, following conversion types are available:
Type	Description
LINEAR	Linear numeric conversion to calculate physical values
HASH	Conversion of numeric values to descriptive state messages. Field Parameters needs to contain: <value>=<state text>[[;<value>=<state text>]...]
BITMAP	Conversion of bit masked values to descriptive bit states. Field Parameters needs to contain: <bit position>=<state text>[[;<bit position>=<state text>]...]
PCODELIST	Conversion of OBD P/I-Fault code numbers to it's fault description. Field Parametrs: <path to codelist file>[[;<path to codelist file>]...]
CODELIST	Conversion from any numerical code number to it's fault description. Field Parametrs: <path to codelist file>[[;<path to codelist file>]...]
ASCII	Conversion from protocol buffer to ASCII string

### Conversion data fields:
Field	Description
CONVERSION_ID	Textual ID of this conversion, which is used as reference for data items to be used
TYPE	Textual ID of the type of conversion. See description of conversion types below ...
VARIANT	ID of variants to the selected conversion type (currently unused, always 0)
SYSTEM	System of measurement: METRIC / IMPERIAL.
FACT	factor for numeric calculation
DIV	divider for numeric calculation
OFFS	offset for numeric calculation
PhOf	physical offset for numeric calculation
UNIT	physical unit representation
Remark	remarks to this data conversion
Parameters	parameter data for non linear/numeric conversions (like state lists, bit descriptions, etc.) in csv list format: <key>=<value>[[;<key>=<value>]...]

### Linear Numeric conversion calculation:
All linear conversion items are calculated using following formula:

        ( rawValue + OFFS ) * FACT
physicalValue= -------------------------- + PhOf
        DIV

## Data items / PIDs:
Data item / PID definitions contain all information to extract certain data elements out of the received communication data buffer like OBD service, OBD PID number, item position and length, together with the information of the data content, conversion and limitation to certain MIN/MAX limits.
Since OBD pids may contain more information, than just one measurement, multiple data items may be extracted/displayed fromout one PID data response.

### Data items / PIDs data fields:
Field	Description
svc	OBD service(s), which this data item is valid for. comma separated list of HEX numbers
pid	OBD PID number which this data item is contained. Single HEX PID number
ofs	Offset (in bytes) where this data is located within PID response payload data
len	Length of data item in bytes within PID response payload data
bit_ofs	Bit offset within extracted value (using above ofs/len parameters)
bit_len	Length of value in bits
bit_mask	Bit mask to extract relevant bits within extracted value
formula	Textual ID of data conversion to be used. See CONVERSION_ID
format	Data display format definition (printf syntax)
min	Minimum limit of value if not specified, limits are calculated automatically from conversion formula
max	Maximum limit of value if not specified, limits are calculated automatically from conversion formula
label	Description label text for data item display

## Data extraction algorithm:
RAW data is extracted from communication buffer using following algorithm:
<RAW value> = (int)( buffer[ofs]...buffer[ofs+len] ) >> bit_ofs & ((1 << bit_len)-1) & bit_mask
# Data customization:
Data customization is a feature which I recommend be used by advanced AndrOBD users only, because inconsistencies in customization data may create inconsistent output or even lead to a program crash. So, if you know what you are doing, please play with it, but don't blame it on me if you don't ;-)

## Purpose:
The purpose of data customization is to allow users to:
- add new custom PIDs / data items if they are not covered yet
- use custom data conversions / scaling
- overrule existing PIDs / data items / conversions
- add new custom fault codes if they are not covered yet
- overrule existing fault codes with custom descriptions

## How to customize:
The customization is done by loading additional configuration data files into the existing data model. These files have to be stored on your device (i.e. /sdcard/com.fr3ts0n.ecu.gui.androbd/custom/) and may be selected in the settings dialogue.
Template sample customization files may be found here:
https://github.com/fr3ts0n/AndrOBD/tree/master/customisation/templates
Please note that - once configured - the files will be loaded at every program startup.
In order to run the original data model again, you will have to clear it out of the configuration by aborting the file selection process for the corresponding setting.
Before modifying the files, please read the chapter „Configuration data“ carefully.

Keep on hacking...
fr3ts0n